APS Research Project
Single Image Haze Removal Using Dark Channel Prior
Submitted by:
Divy Kala
Divyansh Shrivastava
Ankit Gupta

---
Overview
- The dark channel prior is based on a key observation.
- Most local patches in haze-free outdoor images contain some pixels which have very low intensities in at least one color channel.
- If an image is hazy the above does not hold true for the hazy parts (and the parts with sky in it).
- Using this prior with the haze imaging model, we can directly estimate the thickness of the haze and recover a high quality haze-free image.

---
Dark Channel
Where for an image J is the scene radiance,
Jc is a colour channel of J.
Ω(x) is a local patch centered at x.
Jdark is the dark channel, which is dark in all the regions except the sky (and the haze, and other very bright parts).
The dark channel has a special property for hazy images without sky in it.

---
Dark Channel Prior
According to the dark channel prior, the dark channel
Jdark of the haze-free radiance J tend to be zero:

---
Haze image formation model
- I is observed intensity
- J is scene radiance
- A is the global atmospheric light
- t is the medium transmission describing the portion of light not scattered and reaches the camera

---
Estimating the transmission
- Assume that the transmission in a local patch Ω(x) is constant
- We denote the patch’s transmission as t˜(x).
- Taking the min operation in the local patch on the haze imaging equation
- Using the Dark Channel Prior, we take the min operation among three color channels on the above equation and obtain:
- Where (Ic / Ac) is the normalized haze image. Ic is a known quantity, but Ac needs to be estimated.

---
Details:

---
Details:

---
What about the sky region?
- Dark channel prior does not hold good in sky regions.
- Fortunately, the color of the sky is similar to Atmospheric light A in a hazy image. i.e Ic ~ Ac, therefore,
- Sky regions tend to have 0 transmission, this is handled gracefully by our method of estimating transmission t~.
- Hence, sky and non-sky regions are both handled gracefully by the same method of estimating transmission.

---
Aerial Perspective
- Completely haze free images look fake.
- Some haze must be left in the processed image
- We use a parameter ω to permit some haze for distant objects. 0< ω <= 1
- Good values of ω are 0.9 to 0.95

---
Atmospheric Light – The next piece in the puzzle
- The most haze-opaque pixel will give a good idea of the atmospheric light A.
- Because t(x) for this pixel tends to 0.
- Therefore we get I(x) = A

---
Approaches for picking haze-opaque pixels
- The max intensity pixel.
  - The brightest pixel could be a lamp, mirror, etc.
- Using Dark channel
  - Dark channel represents haze-denseness well
  - We first pick the top 0.1% brightest pixels in the dark channel.
  - These pixels are most haze-opaque
  - Among these pixels, the pixels with highest intensity in the input image I is selected as the atmospheric light.
  - This gives us the truly brightest pixels, that are also haze-opaque

---
Atmospheric Light – The next piece in the puzzle

---
Recovering the scene radiance
- With all the pieces in hand, we use Haze Imaging Model to recover scene radiance J:
- t0 is used because J(x)t(x) can become very small for small values of t, making J prone to noise. We use t0 = 0.1.
- Since t(x) has a lower bound, some haze is preserved in very dense haze regions (where transmission is very low).
- Finally, exposure of J may be increased as after haze removal the image looks dim.

---
A high quality depth map can also be obtained as a by-product of haze removal.

---
Results